Information on dataset and sensors

Data and information is coming from PMRF, an instrumented US Navy testing range located off the island of Kauai, Hawaii. Data were collected from seven bottom mounted hydrophones (4 to 5 m off the seafloor) in deep water (nominally 4,600 meters) approximately 45 km northwest of Kauai. The relative location of the hydrophones, their designations and filenames for the data files are as shown in Table 1.
With this dataset you’ll be able to make localization of minke whales (Balaenoptera acutorostrata) based on their boings sounds. You’ll find more info about what the boing sounds look like in the publication by Rankin et al. which I also attach. Beware that vocalizations from other species are also present, we’ll take a look at the data together if necessary.

The dataset is from the 27th of April 2009 at approximately 12:00 Hawaiian standard time. Thirty minutes of data from each hydrophone are provided as three files (approx. 10 minutes per file). The sampling rate of the recordings (windows PCM wav format) is 96 kHz with 16 bits resolution. The data are sampled simultaneously, so sample N from one file is the same relative time as sample N of a second file with the same filename. The file format is .wav in little-endian format.

hydrophone #	X(m)	Y(m)	Z(m)	filenames
7	-6129	9784	-4750	27Apr09_074921_NN_p7.wav
6	-6183	-4874	-4650	27Apr09_074921_NN_p6.wav
5	-6163	-12402	-4600	27Apr09_074921_NN_p5.wav
4	6865	12844	-4750	27Apr09_074921_NN_p4.wav
3	6520	5240	-4650	27Apr09_074921_NN_p3.wav
2	6635	-2132	-4500	27Apr09_074921_NN_p2.wav
1	6566	-9617	-4500	27Apr09_074921_NN_p1.wav

Some examples of time intervals with interesting sounds / (reference file : 27Apr09_174921_026_p2.wav) / (you might also try to localize the delphinids sounds)

Approximative begin (onset) in seconds	Approximative end (offset) in seconds
0:39.392	0:43.156
1:00.441	1:03.557
1:05.503	1:09.092
2:31	2:35
2:05.009	2:09.407
2:30.439	2:36.000
3:29.476	3:34.227
8:48	8 :54
9:08.258	9:11.000
9:28.695	9:34.000